## Slide 1: Creation of a 3-D Gantry System
A Proposal

## Slide 2: Problem
Monitoring and control of a system in one, two, and three dimensions
Development of a third dimension to a two-dimensional gantry system
  EleksLaser-A3 Pro 5500mW Laser Engraving Machine
Difference between cantilever axis and 3-D gantry
  Location of Third Axis
Power and weight of gantry

## Slide 3: Components
Infrared/Ultrasonic Proximity Sensors
  Senix ToughSonic 3 Ultrasonic Sensor
Three-dimensional Tracking Sensor System
20-2020 beams
Stepper Motor
  Nema 23 CNC 2.8A (11lbs holding weight)
3-D printed parts
  Toothed belt custom fit for beam
  Guide for third gantry beam

## Slide 4: First Phase: One Dimension
Elevated axis monitored by proximity sensor on one end
  Less wear on motor
  More precise control
  Can be created using 20-2020 beams and part of the 2-D Gantry
Proximity sensor located on end
  0.086 mm accuracy
  Can be put into place using 3-D printed parts

## Slide 5: Second Phase: Two Dimensions
Complete set-up of 2-D Gantry
Attach second proximity motor to new axis

## Slide 6: Third Phase: Application to 2-D Gantry
“True” 3-D Gantry
  Attachment to Y-Axis
Suspension of original gantry system
  Attached to 20-2020 beams by drilled holes through supports
Third beam attached to laser platform
  Proximity sensor attached to end of third beam

## Slide 7: Final Dimensions of Third Phase
Enclave: 90 cm by 200 cm by 75 cm
Gantry within enclave: 60 cm by 46 cm by 63 cm
Working area: 30 cm by 36 cm by 45 cm
Control of 4 degrees of freedom
  Three axises
  Laser intensity control

## Slide 8: Final Cost
2-D Gantry: $439.90
Proximity Sensors: $1647.00
  Request a Quote
Nema Stepper Motor: $26.00
7 6-foot 20-2020 beams: $94.29
Final Cost: $2207.19 + shipping & tax

## Slide 9: Future Work
Laser module
  Degree of freedom
Implementation of different sensors
  Spatial sensing
  3-D tracking